## Slide 1: Lab 11 and 12: MOSFETs
EE316-08 Spring 2021

## Slide 2
Purpose: The concept and characteristics of Metal Oxide Semiconductor Field Effect Transistors (MOSFETs) are introduced. Both N-channel and P-channel MOSFETs will be considered.

## Slide 3: Background
Metal Oxide Semiconductor Field Effect Transistor (MOSFET) is the most common type of insulated gate FET that designed for switching or amplifying voltages in the circuits.
In other word, MOSFET is a voltage-controlled field effect transistor.
MOSFET has a metal oxide gate electrode which is electrically insulated from the main semiconductor N-channel or P-channel by a thin layer of insulating material.
Therefore, the gate terminal is isolated from the main current carrying channel, and no current flows into the gate.
Structural diagram of N-channel MOSFET

## Slide 4: Background
MOSFETs are three terminal devices with a Gate, Drain, and Source.
The current flowing through the main channel between the drain and source is proportional to the input voltage.
MOSFETs can be made extremely small, can draw very little input current, and consume small power.
Symbolic representation of MOSFETs Under the Depletion Mode
MOSFETs operate in two different modes.
  Depletion Mode: the transistor requires the Gate-Source voltage () to switch the device OFF. The depletion mode MOSFET is equivalent to a normally closed switch.
  Enhancement Mode: the transistor requires a gate-source voltage, () to switch the device ON. The enhancement mode MOSFET is equivalent to a normally open switch.

## Slide 5: Structural Diagram of MOSFETs
N-channel MOSFET
P
P
N
Substrate
P-channel MOSFET
N
N
P
Substrate
Two N-type semiconductors fixed at Drain and Source terminals in the channel region.
The channel between Drain and Source is P-type.
Two P-type semiconductors fixed at Drain and Source terminals in the channel region.
The channel between Drain and Source is N-type.

## Slide 6: Depletion Mode N-Channel MOSFET
1. Ohmic
2. Saturation Region
Ohmic Region: MOSFET acts like a variable resistor.
Saturation Region or Linear Region: MOSFET is strongly influenced by . MOSFET is ON.

## Slide 7: Depletion Mode P-Channel MOSFET

## Slide 8: Enhancement Mode N-Channel MOSFET
1. Ohmic
2. Saturation Region

## Slide 9: Enhancement Mode P-Channel MOSFET

## Slide 10: Figure 11.5: Main Idea
Gate
Drain
Source
An unknown MOSFET (2N7000) is given
Measure (V), (V), (mA)
Plot...
  (V) vs. (mA)
  (V) vs. (mA)
Find out...
  Type of the given MOSFET (N or P)
  Mode of the given MOSFET (Depletion or Enhancement)
Note: This is just the main point for lab 11. There will be sub-questions such as identify threshold voltage, and the minimum values. Please make sure you answer all questions in the lab manual.

## Slide 11: Figure 12.1
Build the circuit in Fig. 12.1 with the input voltage
Find and Gain (dB)
Plot Gain (dB) vs. Frequency (Hz)
  Frequency-axis is in log scale
Identify…
  Bandwidth
Comment on phase relationship

## Slide 12: Gain, Low and High Cutoff Frequencies, and Bandwidth
Chart: Gain (dB) vs. Frequency (Hz)
| 30 | 45 | 60 | 100 | 200 | 500 | 1000 | 10000 | 100000 | 500000 | 1000000 | 1500000 | 2000000 | 3000000 | 4000000 | 5000000 | 7000000 | 10000000 | 11000000 | 12000000 | 15000000 | 16000000
 | 11.8867 | 13.854 | 14.97 | 16.151 | 16.8 | 16.999 | 17.036 | 17.047 | 17.047 | 17.039 | 17.017 | 16.964 | 16.946 | 16.714 | 16.558 | 16.33 | 15.586 | 14.669 | 14.284 | 13.856 | 12.6269 | 12.2967
Chart: Gain (dB) vs. Frequency (Hz)
| 30 | 45 | 60 | 100 | 200 | 500 | 1000 | 10000 | 100000 | 500000 | 1000000 | 1500000 | 2000000 | 3000000 | 4000000 | 5000000 | 7000000 | 10000000 | 11000000 | 12000000 | 15000000 | 16000000
 | 11.8867 | 13.854 | 14.97 | 16.151 | 16.8 | 16.999 | 17.036 | 17.047 | 17.047 | 17.039 | 17.017 | 16.964 | 16.946 | 16.714 | 16.558 | 16.33 | 15.586 | 14.669 | 14.284 | 13.856 | 12.6269 | 12.2967
19
16
7
4
~ 10 Hz
~ 10M
Bandwidth
3 dB
Therefore, Bandwidth = -
Frequency | () | Gain (dB)
10 |  | 
30 |  | 
60 |  | 
100 |  | 
200 |  | 
500 |  | 
1000 |  | 
2000 |  | 
5000 |  | 
10000 |  | 
15000 |  | 
20000 |  | 
50000 |  | 
75000 |  | 
100000 |  | 
150000 |  | 
200000 |  | 
500000 |  | 
750000 |  | 
1000000 |  | 
1500000 |  | 
2000000 |  | 
3000000 |  | 
Frequency |  | Gain (dB)
10 |  | 
30 |  | 
60 |  | 
100 |  | 
200 |  | 
500 |  | 
1000 |  | 
2000 |  | 
5000 |  | 
10000 |  | 
15000 |  | 
20000 |  | 
50000 |  | 
75000 |  | 
100000 |  | 
150000 |  | 
200000 |  | 
500000 |  | 
750000 |  | 
1000000 |  | 
1500000 |  | 
2000000 |  | 
3000000 |  | 

## Slide 13: Figure 12.1: Find (Recall)

## Slide 14: Example: Find
Frequency (Hz) | Measured Vout (mVpeak) | Gain (dB) | Gain (ratio) | Calculated Vout (mVpeak)
10 |  | 4.32 | 1.6443 | 164.43
Step 2: Find Vout
Given
Step 1: Find Gain(ratio)
43

## Slide 15: Summary
Lab 11 and 12 Report is due Tuesday 20th April 2021 by midnight.
Final Exam will be available from Tuesday 20th April 2021 to Tuesday 27th April 2021.
Fill out Table 11.1, 11.2 and 12.1 with results from…
  Simulation
  Experimental results

## Slide 16: Reference
Electronic Devices and Circuit Theory, 7th Ed. by Robert Boylestad and Louis Nashelsky.