## Slide 1: Lab 7 and 8: Characteristics of BJT and Amplification Behavior
EE316-08 Spring 2021

## Slide 2
Purpose: The concept and characteristics of bipolar junction transistors (BJTs) is introduced. The basic concepts investigated for BJTs carries over into future labs, especially for MOSFETs. Both NPN and PNP constructions will be considered. Constants and variables relating to BJTs will be discussed and utilized in the procedure section.

## Slide 3: Transistors Background
Transistor is a semiconductor device used as amplifier control or electrically controlled switch.
Transistors can be found in switching circuits, amplifier circuits, voltage-regulator circuits, etc.
Two basic types of transistors are bipolar junction transistors (BJTs) and field-effect transistors (FETs).
The main difference between BJTs and FETs is that BJTs are current-controlled while FETs are voltage-controlled.
Physical and symbolic representation of BJTs
Symbolic representation of FETs

## Slide 4: Bipolar Junction Transistors (BJTs)
BJT is the oldest and the most basic transistor.
It is a solid-state current-controlled device used to electronically switch a circuit.
BJT is a three-terminal device with emitter (E), base (B), and collector (C).
The current applied to the base (B) controls the current flow through the emitter (E) and collector (C).
Symbolic representation of BJTs
NPN
PNP

## Slide 5: Physical Representation of BJTs
NPN
PNP
Current
Current

## Slide 6: Bipolar Junction Transistors (BJTs)
BJT is formed by three layers of semiconductor materials.
  PNP transistor has two P-type regions and one N-type region.
  NPN transistor has two N-type regions and one P-type region.
NPN
PNP
Current
Current

## Slide 7: Characteristics of each region of operation
Cuttoff Region
  Transistor acts like open switch.
  No current flow through the device.
  .
Forward Active Region
  Transistor is on.
  Transistor acts as a linear amplifier.
  is proportional to by a constant called beta. Thus, we will observe the following equation
  High voltage gain and high beta
1.
2.
3.
4.

## Slide 8: Characteristics of each region of operation
Reverse Active Region
  Poor beta.
  Not useful for any applications.
Saturation Region
  Transistor acts like a closed switch.
  does not depend on
  reaches a maximum.
Breakdown Region
  and exceed specification and cause damage to the transistor.
1.
2.
3.
4.

## Slide 9: Useful Equations
NPN
PNP

## Slide 10: Figure 7.3
Chart: Characteristic Curve for a Bipolar Transistor
| 7.9349999999999993E-3 | 8.6999999999999994E-2 | 0.121 | 0.161 | 0.29899999999999999 | 0.54600000000000004 | 0.79300000000000004 | 1.0409999999999999 | 1.2889999999999999 | 2.2789999999999999 | 3.27 | 4.26 | 5.2510000000000003
IB = 11 uA | 0.00794 | 0.163 | 0.379 | 0.589 | 0.701 | 0.704 | 0.707 | 0.709 | 0.711 | 0.721 | 0.73 | 0.74 | 0.749
IB = 31 uA | 0.0136 | 0.188 | 0.417 | 0.652 | 0.89 | 1.13 | 1.37 | 1.6 | 1.84 | 2.06 | 2.23 | 2.25 | 2.25 | 2.26 | 2.27 | 2.28 | 2.28 | 2.31 | 2.34 | 2.37 | 2.39
Base
Collector
Emitter
V1 = 4 V
V1 = 10 V

## Slide 11: Figure 8.1: Find Vout
Don’t forget Vcc

## Slide 12: Table 8.1: Example
Frequency (Hz) | Calculated Vout (mVpeak) | Gain (ratio) | Gain (dB) | Simulated Vout (mVpeak)
10 | 0.141 | 0.00056 | -64.97 | 0.138
30 | 0.424 | 0.00169 | -55.42 | 0.420
Step 2: Find Vout
Given
Step 1: Find Gain(ratio)

## Slide 13: Summary
Lab 7 and 8 Report is due Thursday 25th March 2021 by midnight.
Prelab 9 and 10 is due Tuesday 30th March 2021 by midnight.
Fill out Table 7.1 and 8.1 with results from…
  Simulation
  Experimental results

## Slide 14: Reference
Electronic Devices and Circuit Theory, 7th Ed. by Robert Boylestad and Louis Nashelsky.