## Slide 1: Lab 3: Op-Amp Integrator and Differentiator Circuits
EE316-08 Spring 2021

## Slide 2
Purpose: The goal of this laboratory is to examine the circuit characteristics of the Op-Amp Integrator and Op-Amp Differentiator circuits.

## Slide 3: ‘Ideal’ Operational Amplifier
where:
A is a constant called the open-loop gain
* For an ideal amplifier, A is infinite
The inverting input terminal
The noninverting input terminal
Summary for an ideal op-amp:
Current at the inverting input terminal is equal to zero
Current at the noninverting input terminal is equal to zero
, therefore,
The input impedance of an ideal op-amp is infinite ()
The output impedance of an ideal op-amp is zero ()

## Slide 4: Integrator
The input signal is integrated at the output.
One problem of circuit in Fig. 3.1 is that the output tends to drift due to nonlinear characteristics of real op-amps such as voltage offset.
The integrator is useful for turning square waves into triangular waves, and triangular waves into sine waves.
The integrator’s output voltage is
Integrated input
Scale input

## Slide 5: Integrator
Input Signal: Sine waves
Output Signal: Cosine waves
Input Signal: Square waves
Output Signal: Sine waves
Input Signal: Triangular waves
Output Signal: Triangular waves
Voltage Offset
NOTE: Results depend on your R, C and frequency values

## Slide 6: Differentiator
The differentiator does the opposite of the integrator.
The input signal is differentiated at the output.
Disadvantages of circuit in Fig. 3.2 are susceptible to noise and instability at high frequency.
The differentiator output voltage is
Take derivative of input
Scale

## Slide 7: Differentiator
Input Signal: Sine waves
Output Signal: Cosine waves
Input Signal: Square waves
Output Signal: Spike (approx. to dirac delta function)
NOTE:
R = 10K
C = 0.1nF
Input Signal: Triangular waves
Output Signal: Square waves
NOTE:
R = 10
C = 0.1uF
Noisy
NOTE: Results depend on your R, C and frequency values

## Slide 8: Summary
Lab 3 Report & Pre-lab 4 are due on Tuesday 9th February 2021 by midnight.
Analyze Fig. 3.1-3.2
  Simulation
  Calculations (Bonus Point)
  Experimental section