## Slide 1: CPE 323 Intro to Embedded Computer Systems System Architecture
Aleksandar Milenkovic
milenka@uah.edu

## Slide 2: Admin

## Slide 3: CPU, Memory, Peripherals, Bus (MAB, MDB)

## Slide 4: MSP430FG4618 Block Diagram

## Slide 5: MSP430xG461x Microcontroller

## Slide 6: MSP430F5529
A quad flat package (QFP) – surface mounted IC package, leads extend on all 4 sides: LQFP (low profile QFP), TQFP (thin QFP)
PN – Texas Instruments name of the package

## Slide 7: Pin Diagram for MSP430F5529

## Slide 8: Clock Subsystem
Generate clocks used by components on the chip
  Configured and tuned by software, enable/disable clocks for Low-Power Modes
Multiple types (FLL+, Basic Clock Module)
Three clocks are available:
  Main clock (MCLK): CPU, DMA, selected peripherals
  Sub-system clock (SMCLK): peripherals
  Auxiliary clock (ACLK): peripherals

## Slide 9: Watchdog Timer
Monitors system operation
Two modes of operation
  Watchdog
  Interval timer
Watchdog: performs controlled system reset if a software error occurs
Interval timer: generates an regular periodic interrupt
Active on power-up

## Slide 10: Timers (Timer_A, Timer_B)
Time keeping
  Timer block: counter
  Capture&Compare block: logic where action occurs
Two main functions
  Capture
  Compare
Capture: monitor external events (signal transitions) and timestamp them when a change is detected
Compare: produce PWM signals, compare running counter to predefined values in CCRx and trigger a change in a signal

## Slide 11: Comparator (Comparator_A)
Compare an analog signal to a reference voltage and produces a binary output (1 if VinVref, 0 otherwise)
Supports precision slope analog-to-digital conversions
Supply voltage supervision
Monitoring of external analog signals

## Slide 12: Analog-to-Digital Converter (ADC12)
Convert analog signals to binary counterparts
ADC12:
  12-bit resolution
  200 Ksamples/s
  8 external inputs
  Local memory
  Programmable sample time
  Selectable reference voltages

## Slide 13: Serial Communication Interfaces (USCI, USART, USI)
Support for synchronous and asynchronous serial communication
UART
SPI
I2C
Infrared

## Slide 14: TI Experimenter’s Board: Block Diagram
Microcontroller’s (F4618, F2013)
JTAGs
Buttons/Switches
Capacitive Touch Pad
Microphone
Buzzer
LCD
Wireless Interface
RS232

## Slide 15: TI Experimenter’s Board
Two on-board CPUs
  MSP430FG4618
  MSP430F2013
The Softbaugh SBLCDA4 LCD display
  4-MUX operation and is interfaced to the MSP430FG4618 LCD driver peripheral
Momentary Push-ON Buttons
  S1 and S2 are connected to pins on Port 1 (P1) of the MSP430FG4618
Light Emitting Diodes (LEDs)
  Four LEDs, three of which are connected to the MSP430FG4618, and one connected to the F2013.
Buzzer
  Connected to one of the MSP430FG4618 port pins and can be disabled using jumper JP1

## Slide 16: TI Experimenter’s Board
Single-Touch Capacitive Sensing Interface
  A 16-segment touch pad in the shape of a “4” is connected to the data pins of the MSP430F2013, which then relays the data to the MSP430FG4618 using the inter-processor communications peripherals on each CPU
RS232 Serial Communication Port
  A standard 9-pin serial communications port is connected to the MSP430FG4618 USCI peripheral and can be used when the USCI is configured in UART mode
Microphone & Analog Out
  A microphone is connected to a port pin of the MSP430FG4618, and the input to the 3.5mm analog out can be connected to the output from the MSP430FG4618’s 12-bit digital to and analog (DAC12) convertor
Radio
  Wireless Communication Module Interface

## Slide 17: Headers

## Slide 18: Capacitive Touch Pad

## Slide 19: Power Supply Configuration, RF Daughter Card Connect, Audio Output

## Slide 20: MSP430FG4618

## Slide 21: RS232 Connector, LCD Display

## Slide 22: Blink a LED Program
/****************************************************************************
; TI Experimenter board demo, blinking leds LED1 and LED2 (msp430FG4618)
; Description: Toggle P2.1 and P2.2 by xoring P2.1 and P2.2 inside a loop.
; The LEDs are connected to P2.1 and P2.2 and are on when
; P2.1=1 and P2.2=1;
; The LEDs are initialized P2.1 to be off, and P2.2 to be on;
; ACLK = 32.768kHz, MCLK = SMCLK = default DCO
; MSP430xG461x
; -----------------
; /|\| |
; | | |
; --|RST |
; | P2.2|-->LED1(GREEN)
; | P2.1|-->LED2(YELLOW)
; Alex Milenkovich, milenkovic@computer.org
;****************************************************************************/
#include "msp430xG46x.h"
void main(void)
{
WDTCTL = WDTPW + WDTHOLD;// Stop watchdog timer
P2DIR |= 0x06; // Set P2.1&P2.2 to output direction (0000_0110)
P2OUT = 0x02; // Set P2OUT to 0x0000_0010 (LED2 is on, LED1 is off)
for (;;) {
unsigned int i;
P2OUT ^= 0x06; // Toggle P2.1 using exclusive-OR
i = 50000; // Delay
do (i--);
while (i != 0);
}
}